## Slide 1: CS2105 Introduction to Computer Networks Tutorial 6

## Slide 2: Recap
Network Address Translation (NAT)
Each interface in local network has IP address in reserved range
  10.0.0.0/8  10.0.0.0 to 10.255.255.255
  172.16.0.0/12  172.16.0.0 to 172.31.255.255
  192.168.0.0/16  192.168.0 0 to 192.168.255.255
Router maintains one external IP address
  Each local IP/port is mapped to an external port
  Different hosts on same local network have same external IP address
  Router needs to store NAT table in memory

## Slide 3: Recap
IP Datagrams:
Header + Data
  Data may be split up according to MTU of links
  New header added to each smaller “part”
  Length includes header!

## Slide 4: Recap
IP Datagrams:
Offset
  First “byte number” of data in multiples of 8-bytes
Frag Flag
  Signifies when fragment is last fragment of original IP datagram
Header: 20
Data: 1180

## Slide 5: Question 1
Consider the network setup in the following figure. Suppose that the ISP assigns the router the address 24.34.112.235 and that the network address (i.e. network prefix) of this home network is 192.168.1/24.

## Slide 6: Question 1
a) Give an example IP address assignment to all interfaces in this home network.

## Slide 7: Question 1
b) Suppose each host has two ongoing TCP connections, all to port 80 of a server at 128.119.40.86. Provide example corresponding entries in the NAT translation table.

## Slide 8: Question 1
Hint
NAT routers must: Replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #).
Replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT translation table.

## Slide 9: Question 1

## Slide 10: Question 2
Consider sending a 1500-byte IP datagram into a link that has an MTU (Maximum Transmission Unit) of 500 bytes. Suppose the original datagram is stamped with the identification number 422. Also assume that IP header is 20 bytes long.
How many fragments will be generated?
Data (segment) length = 1500 – 20 = 1480 (due to 20 bytes IP header)
Maximum size of data in each fragment = 500 – 20 = 480
Number of fragments = ⌈1480/480⌉ = 4

## Slide 11: Question 2
b) What is the length of each fragment (including IP header)?
1st – 3rd fragments have length 500. 4th fragment has length 60.
(
total data you need to send = 1480 bytes
Total data sent in the first 3 fragments = 480 * 3 = 1440 bytes
Last fragment contains 1480-1440 = 40 bytes of DATA
After adding 20 bytes of HEADER, total length of 4th fragment = 60
)

## Slide 12: Question 2
c) What are the values of identification number, offset and flag in each fragment?

## Slide 13: Question 2
Hint
  ID number same for whole datagram/segment
  Flag (fragment flag) is set to
    1 if there is next fragment from the same segment.
    0 if this is the last fragment.
  Offset is in expressed in unit of 8-bytes.
    Eg: Fragment 1: offset =0
      Fragment 2 :offset = 60 ( 60* 8 = 480 bytes)
      Fragment 3: offset = 120 ( 120 * 8 = 960)

## Slide 14: Question 2
0
480
960
1440
First byte of segment

## Slide 15: Question 2
Length: 1500 (1480+20) | ID=422 | Flag=0 | Offset=0
Length: 500 (480+20) | ID=422 | Flag=1 | Offset=0
Length: 500 (480+20) | ID=422 | Flag=1 | Offset=60
Length: 500 (480+20) | ID=422 | Flag=1 | Offset=120
Length: 60 (40+20) | ID=422 | Flag=0 | Offset=180

## Slide 16: Question 3
The following diagram shows a simple network topology with 4 nodes. The links in the diagram are labeled with the cost of each link. The nodes run distance vector routing protocol. The protocol has terminated, and each node knows the cost of the minimum cost path to every other node.

## Slide 17: Question 3

## Slide 18: Node x before 1st iteration
 | Cost to w | Cost to x | Cost to y | Cost to z
From x | 3 | 0 | 3 | 6
From y | 7 | 3 | 0 | 2
From z | 20 | 6 | 2 | 0
From w | 0 | 3 | 7 | 20

## Slide 19: Node x
dx(x) =0
dx(y) = min{c(x,y)+ dy(y), c(x,w)+dw(y), c(x,z)+dz(y)}
      min { 3+0, 3+7,6+2} = 3
dx(w) = min{c(x,w)+ dw(w), c(x,y)+dy(w), c(x,z)+dz(w)}
      min { 3+0, 3+7,6+20} = 3
dx(z) = min{c(x,z)+ dz(z), c(x,y)+dy(z), c(x,w)+dw(z)}
      min { 6+0, 3+2,3+20} = 5
 | Cost to w | Cost to x | Cost to y | Cost to z
From x | 3 | 0 | 3 | 6
From y | 7 | 3 | 0 | 2
From z | 20 | 6 | 2 | 0
From w | 0 | 3 | 7 | 20

## Slide 20: Node x after updating
 | Cost to w | Cost to x | Cost to y | Cost to z
From x | 3 | 0 | 3 | 5
From y | 7 | 3 | 0 | 2
From z | 20 | 6 | 2 | 0
From w | 0 | 3 | 7 | 20

## Slide 21: Node y
dy(y) = 0
dy(x) = min{c(y,x)+ dx(x), c(y,w)+dw(x), c(y,z)+dz(x)}
      min { 3+0, 7+3, 2+6} = 3
dy(w) = min{c(y,w)+ dw(w), c(y,x)+dx(w), c(y,z)+dz(w)}
      min { 7+0, 3+3, 6+20} = 6
dy(z) = min{c(y,z)+ dz(z), c(y,x)+dx(z), c(y,w)+dw(z)}
      min { 2+0, 3+6, 7+20} = 2
 | Cost to w | Cost to x | Cost to y | Cost to z
From x | 3 | 0 | 3 | 6
From y | 7 | 3 | 0 | 2
From z | 20 | 6 | 2 | 0
From w | 0 | 3 | 7 | 20

## Slide 22: Node x table with the shortest distance
 | Cost to w | Cost to x | Cost to y | Cost to z
From x | 3 | 0 | 3 | 5
From y | 6 | 3 | 0 | 2
From z | 8 | 5 | 2 | 0
From w | 0 | 3 | 6 | 8

## Slide 23: Question 3

## Slide 24: Question 4
Do the following:
1. Start up Wireshark and begin packet capture.
2. Start up the Terminal and execute the following command:
  ping www.google.com (Windows) OR Ping www.google.com -c 4 (Linux/mac)
3. Stop Wireshark packet capture.
4. Type in “icmp” into the display filter specification window, then select Apply

## Slide 25: Question 4
1. Within the IP packet header, what is the value in the upper layer protocol held?
ICMP.

## Slide 26: Question 4
2. Which fields in the IP datagram always change from one datagram to the next within this series of ICMP messages sent by your computer?
Identification and Checksum.

## Slide 27: End of Tutorial